SANE Short Term Run Plan – Sun. 3/15 owl/day/eve

RUN PLAN (SAVE previous run plans in the Run Plans binder)

Sun. 3/15 owl/day/eve. Opportunistic accesses: when switching targets, during anneals (check with the target experts) or to delay or move up anneal times to avoid annealing between midnight and 6:00 AM. Keep < 30 min. long if possible.

HMS: it has been set HMS to new kinematics.

BEAM (for production runs):
Current : 85 to 105 nA
- check that the SR is ON and configured for 20 mm diameter, 4.7 GeV beam. Wavetek generators Preset 5: spiral = 1.16 V; circles 1 & 2 = 1.10 V
- fast raster 1 x 1 mm
beam at x = 0.0 (+/- 0.1), y = 1. mm on BPM 3H00A;
x = -1.0 (+/-0.1), y = 1. mm on BPM 3H00B
DATA:

HMS: check that it is set at 3.2 GeV, 20.2, electrons.

Make sure all detectors are ON, LED's off and retracted, prescale factors and trigger type correct, etc. before starting

Put the Bottom target in the beam. Ask MCC for 70 nA and check centering of the beam on the target by looking at the slow raster y vs x ADC plot. Watch for the target cup rims showing as bright areas on the raster ADC plot.
Take data with BOTTOM target POSITIVE polarization.

If the polarization rises above 60% in  30 min, wait until it is at least 75% or 45 min, whichever comes first, and then ask for 90 nA, take ~1 h long runs. If the polarization continues to increase with beam, ask for 100 nA, but reduce the current back to 90 nA once the maximum polarization is attained. When the polarization is around 62% take data at 105 nA. Continue with 1 h runs until the polarization is at ~ 0.75 of its maximum value or 60%, whichever is higher. Move to the BOTTOM target.

- If the polarization takes more than 30 min to get to 50%, it might improve with beam. Ask for 105 nA and start taking data.
  - If the polarization increases with beam continue at 105 nA for up to one hour after the polarization starts dropping, then take data at 90 nA until the polarization drops below 60%.
  - If the polarization does not increase after 2 h of beam, move to the BOTTOM target.
- If the polarization rises quickly but it does not get significantly above 70%, and it starts dropping as soon as beam is turned on, it may have been underannealed. Take data at 85 nA. When the polarization is down to around 62% take data at 95 nA. Move to the TOP target when the polarization drops below 60%.
- Take data with TOP target NEGATIVE polarization.
Follow the guidelines for the BOTTOM target . Anneal when the polarization is at the low limits indicated on the guidelines.

ANNEAL
1. Target experts will conduct the anneal.
2. Put C target in beam to help boiling off He in the nose. Ask for 120 nA. Take data while the nose is emptying (C+He). Turn the beam off when the nose is empty, to start anneal.
3. Target experts will finish the anneal.