Procedure When Changing Targets
NOTE: 'No Target' and ALL Carbon Targets should have Beam at
XCHole = 0.0 mm YCHole = 0.0 mm
- Moving to Pol 3He Cell
  - Tell MCC you are changing target to the Carbon Foil
  - Ask them to restore 5 uA CW and move the beam to
    - X:	0.0 mm
    - Y:	-1.0 mm
      *PolHe3 Beam Position
  - Verify beam position is correct and stable
  - Tell MCC you are moving to the Pol 3He Cell
  - Ask for beam again
- Moving to Reference Cell
  - Tell MCC you are changing target to the Carbon Foil
  - Ask them to restore 5 uA CW and move the beam to
    - X:	-2.0 mm
    - Y:	0.0 mm
      *Reference Beam Position
  - Verify beam position is correct and stable
  - Tell MCC you are moving to the Reference Cell
  - Ask for beam again
Updated: 06 Aug 2020
Ref Cell is @
XCHole – 2.0mm
YCHole + 0.0mm
Pol 3He Cell is @
XCHole + 0.0mm
YCHole - 1.0mm