Update from G4MC Sim
First Usable Results
Allison Zec
2022-04-26

---
Geometry
Previous Run
Current Run

---
Geometry
- HMS Detector
  - Small virtual detector insider HMS collimator bore
  - Too low statistics to be useful (i.e., 50 hits per 106 events on target
- Virtual Detectors
  - Two thin vacuum planes one right behind the other
  - View hits on first plane
  - 2 m away from pivot at 15°
  - 76.2 cm width x 91.4 cm height
  - Angle coverage: 4.2° to 25.8°
HMS Detector
Virtual Detectors
Upstream Target Detector

---
Detector Hit Map
Selection criterion =
Front plane detector only
Units in mm, seen from along z-axis
All hits from electron primaries

---
Momentum Distribution
Units in GeV
Momentum off of gun = 1.159 GeV

---
Momentum vs Radial Distance from Beamline
Y axis in GeV, X axis in mm

---
Conclusions in Brief
- Inbuilt virtual detector package can produce physics results
  - Geometry/placement of detector controlled by config files
- Momentum distribution indicates some physics happening at target
- HMS-collimator detector not yet useful